## Slide 1
Technical Presentation

## Slide 2: Agenda
Overview of Technical Tasks
Development Stages
Demo

## Slide 3: Overview of Technical Tasks

## Slide 4: Development Stages
Phase 1 | Circuit Design & Data Collection
Phase 2 | Implementing Sleep and Wake-on-Interrupt
Phase 3 | ML Model Training & Testing
Phase 4 | Deployment Module

## Slide 5: Phase 1 | Circuit Design & Data Collection
  Sensor Circuit:
    MPU6050
  Microcontroller & Data Storage:
    Pico & Emulated-EEPROM
    Pico with Adalogger & SD Card
  Data Collection
  Data Flow in Software

## Slide 6: Phase 1 | Sensor Circuit
MPU6050 IMU
Advantages:
Low Cost
Low Power Consumtion
Interrupt on Significant Motion

## Slide 7: Phase 1 | Microcontroller & Data Storage
Pico & Emulated-EEPROM
Blocker:
EEPROM Capacity: Limited to only 4KB
Flash Memory: 2MB, also lacks a dedicated EEPROM
Write Limitations: Restricted number of writes affecting continuous data collection

## Slide 8: Phase 1 | Microcontroller & Data Storage
Pico & Adalogger
I2C Bus 1: Real-Time Clock Data
I2C Bus 2: Accelerometer sensor
Write both data to SD Card via SPI
Accelerometer ODR: 100Hz
Gathering data from accelerometer and RTC and writing to SD card.

## Slide 9: Phase 1 | Power Management
Advantageous:
Battery Powered
High Storage Capacity: Stores approx. 1.33 million acc data cycles (~3.7 hours of continuous data at an ODR of 100Hz).
Fast Write Time: Less than 10ms, preventing data loss and increasing efficiency.
Lipo Pico & Flash Memory

## Slide 10: Phase 1 | Data Collection
Linear
Still
Ramp Up
Ramp Down
Required Trajectory

## Slide 11: Phase 1 | Data Flow in Software

## Slide 12: Phase 2 | Implementing Sleep and Wake-on-Interrupt
Earl‘s Arduino Core did not natively support Sleep Functionality
A new Arduino core was built on top of Earls core including the Sleep functionality from Raspberry Pico SDK
This enabled us to use the function sleep_goto_dormant_until which put pico to sleep until there is an interrupt in the particular GPIO pin.

## Slide 13: Phase 3 | ML Model Training & Testing
Data Acquisition & Preprocessing
Feature Extraction
ML Model Development
Model Testing & Regularization
TinyML Model Deployment
Garbage empty process recognition using Tiny ML

## Slide 14: Phase 3 | ML Model Training & Testing
Data Collection and Cleaning

## Slide 15: Phase 3 | ML Model Training & Testing
Feature Extraction for Classification

## Slide 16: Phase 3 | ML Model Training & Testing
Classification
Accuracy

## Slide 17: Phase 3 | ML Model Regularization

## Slide 18: Phase 3 | ML Model Training & Testing
Test Results:

## Slide 19: Phase 4 | Deployment
  Integrate TinyML Model with Sleep Functionality & NodeMCU
  IoT Dashboard
  Software Flowchart
  Enclosure and Mounting

## Slide 20: Integrate TinyML Model with Sleep Functionality & NodeMCU
  Hardware Setup:

## Slide 21: Phase 4 | IoT Dashboard
Arduino Cloud IoT

## Slide 22: Phase 4 | Software Flowchart

## Slide 23: Phase 4 | Enclosure and Mounting
Height | Length | Breadth
6 cm | 17 cm | 8 cm

## Slide 24: Learning Outcomes
Communicaiton Protocols – I2C | SPI
Building Core for Arduino IDE | GCC (LINUX) based compilation
ML Data Preprocessing
ML Algorithms
Testing Procedure | Software Development techniques
IOT
Power Management strategies.

## Slide 25: Future Scope
Improvisation/Regularization of ML Model for better accuracy
Integration of low power communication protocol to notify Facility Managers(e.g. NB-IOT)
Implementation of Acceleration sensor with better interrupt generations (Tilt Motion)
Mounting the Device on the Garbage Can for real data and demonstration

## Slide 26: Demo

## Slide 27: Any Questions?